        Kernel Capabuliti Activities

        I2C-EEPROM

Testing Tools :

-> check patches
-> cloc
-> kloc
-> clang

24C02B :- 2Kb I2C Serial EEPROM

* The Microchip Technology Inc. 24C01B and 24C02B are 1K bit and 2K bit Electrically Erasable PROMs.
* After generating a START condition, the bus master transmits the slave address consisting of a 4-bit device code (1010) for the 24C01B/02B, followed by three
don't care bits.
* The eighth bit of slave address determines if the master device wants to read or write to the 24C01B/02B.

device address: 1010000
For read will be: 10100001
For write will be : 10100001

Features :
• Low-voltage and Standard-voltage Operation
– 1.8 (V
CC = 1.8V to 5.5V)
• Internally Organized 256 x 8 (2K)
• Two-wire Serial Interface
• Schmitt Trigger, Filtered Inputs for Noise Suppression
• Bidirectional Data Transfer Protocol
• 1 MHz (5V), 400 kHz (1.8V, 2.5V, 2.7V) Compatibility
• Write Protect Pin for Hardware Data Protection
• 8-byte Page (2K) Write Modes
• Partial Page Writes Allowed
• Self-timed Write Cycle (5 ms max)
• High-reliability
– Endurance: 1 Million Write Cycles
– Data Retention: 100 Years
• 8-lead PDIP, 8-lead JEDEC SOIC, 8-lead Mini-MAP (MLP 2x3), 5-lead SOT23,
8-lead TSSOP and 8-ball dBGA2 Packages
• Lead-free/Halogen-free
• Die Sales: Wafer Form, Waffle Pack and Bumped Wafers

Raspberry PI 3 :

* There are two giant upgrades in the Pi 3.  The first is a next generation Quad Core Broadcom BCM2837 64-bit ARMv8 processor, making the processor speed increase from 900 MHz on the Pi 2 to up to 1.2GHz on the Pi 3

zImage: a compressed version of the Linux kernel image that is self-extracting. uImage: an image file that has a U-Boot wrapper (installed by the mkimage utility) that includes the OS type and loader information. A very common practice (e.g. the typical Linux kernel Makefile) is to use a zImage file
The name bz in bzImage is misleading!! It stands for "Big Zimage". The "b" in bzImage is "big". Both zImage and bzImage are compressed with gzip. The kernel includes a mini-gunzip to uncompress the kernel and boot into it.

i2c_client.c :
*A driver structure contains general accessroutines, and should be zero-initialized except for fields with data you provide.

*A client structure holds device-specific information like the driver model device node, and its I2C address.

*You can use MODULE_ALIAS (passing "foo" in this example) to add
another name for the module. If the driver name doesn't match the module
name, the module won't be automatically loaded (hotplug/coldplug).
I2C device drivers using this binding model work just like any other
kind of driver in Linux: they provide a probe() method to bind to
those devices, and a remove() method to unbind.

        static int foo_probe(struct i2c_client *client,
        const struct i2c_device_id *id);
        static int foo_remove(struct i2c_client *client);

Remember that the i2c_driver does not create those client handles. The
handle may be used during foo_probe(). If foo_probe() reports success
(zero not a negative status code) it may save the handle and use it until
foo_remove() returns. That binding model is used by most Linux drivers.

The probe function is called when an entry in the id_table name field
matches the device's name. It is passed the entry that was matched so
the driver knows which one in the table matched.
I2C and SMBus Subsystem:
*Most I2C devices use seven bit addresses, and bus speeds of up to 400 kHz; there’s a high speed extension (3.4 MHz) that’s not yet found wide use.

*I2C is a multi-master bus; open drain signaling is used to arbitrate between masters, as well as to handshake and to synchronize clocks from slower clients.

Members
class
What kind of i2c device we instantiate (for detect)
attach_adapter
Callback for bus addition (deprecated)
probe
Callback for device binding - soon to be deprecated
remove
Callback for device unbinding
probe_new
New callback for device binding
shutdown
Callback for device shutdown
alert
Alert callback, for example for the SMBus alert protocol

command
Callback for bus-wide signaling (optional)
driver
Device driver model driver
id_table
List of I2C devices supported by this driver
detect
Callback for device detection
address_list
The I2C addresses to probe (for detect)
clients
List of detected clients we created (for i2c-core use only)
disable_i2c_core_irq_mapping
Tell the i2c-core to not do irq-mapping
# difference between the following kernel terms: vmlinux, vmlinuz, vmlinux.bin, zimage & bzimage?
vmlinux
This is the Linux kernel in an statically linked executable file format. Generally, you don't have to worry about this file, it's just a intermediate step in the boot procedure.
The raw vmlinux file may have usage for debugging purposes.
vmlinux.bin
The same as vmlinux, but in a binary file format.
vmlinuz
The vmlinux file usually gets compressed with zlib. Since 2.6.30 LZMA and bzip2 are also available. By adding further boot and decompression functionalities to vmlinuz, the image can be used to boot a system with the vmlinux kernel.
The compression of vmlinux can occur with zImage or bzImage. The function decompress_kernel() handles the decompression of vmlinuz at bootup, a message indicates this:
Decompressing Linux... done
Booting the kernel.
zImage (make zImage)
This is the old format for small kernels (compressed, below 512KB). At boot, this image gets loaded low in memory (the first 640KB of the RAM).
bzImage (make bzImage)
The big zImage (this has nothing to do with bzip2), was created while the kernel grew and handles bigger images (compressed, over 512KB). The image gets loaded high in memory (over 1MB of the RAM).
As today's kernels are way over 512KB, this is mostly the preferred way

write how many bytes want to write
88

write how many bytes want to read
513
 give the input starting value
500
 enter 1 for write same byte in all locations
 enter 0 for write different random byte in all locations
0
 /dev/eeprom Opened
Invoking Write
Invoking Read
Error:Read failed

### What is an EEPROM?
EEPROM stands for electrically erasable programmable read-only memory. It is a non-volatile flash memory device, that is, stored information is retained when the power is removed. EEPROM generally offers excellent capabilities and performance. In EEPROM we can write and program the IC for many times and these are acting as EPROM (UV erasable programming ROM).
### Features of EEPROM:
- Low and standard voltage operation (100 kHz (1.8V) and 400 kHz (2.7V, 5V) compatibility)
- Schmitt trigger, filtered inputs for noise suppression
- Internally Organized 128 x 8 (1K), 256 x 8 (2K), 512 x 8 (4K), 1024 x 8 (8K) or 2048 x 8 (16Kwrite how many bytes want to write
- 88
- write how many bytes want to read
- 513
- give the input starting value
- 500
- enter 1 for write same byte in all locations
- enter 0 for write different random byte in all locations
- 0
- /dev/eeprom Opened
- Invoking Write
- Invoking Read
- Error:Read failed )
- Automotive devices available
- Two-wire serial interface (Two wires are used to read and write data into it)
- Bidirectional data transfer protocol
- Write protect pin for hardware data protection
- 8-byte page (1K, 2K), 16-byte page (4K, 8K, 16K) write modes
- Partial age writes allowed
- Self-timed write cycle
### Applications of EEPROM
EEPROMs are used in many applications such as telecom, consumer, automotive and industrial applications. The other applications are include:
1. The reprogrammable calibration data for test equipment
2. Data storage from a learn function as in a remote control transmitter.
#### AT24C02 EEPROM:
The AT24C02 is an electrically erasable programmable read-only memory (EEPROM) chip. It is internally organized with 32 pages of 8 bytes each; it has 2Kbits of memory size. It is most commonly used EEPROM; it comes with 8-pin DIP, shown in figure:

Pin 1-3: A0, A1, A2 are the address inputs of chip, in this A1 and A2 are for addressing and A0 is a NA (no connection) pin. The eight 2K devices may be addressed on a single bus system.
Pin 4: Ground (GND).
Pin 5: It is a serial data pin; it is bi-directional for serial data transfer.
Pin 6: It is serial clock input, provides the positive clock signals.
Pin 7: It is write protect pin, provides the hardware data protection. It allows read/write operation when connected to ground pin.
Pin 8: Power supply.
### Application involving EEPROM 24C02
 From the circuit, in this we used EEPROM 24C02 of 2KB memory to store the desired password/number entered by the keypad, both of which are interfaced to microcontroller shown in figure. While the user wants to open the lock which is prompted by an LCD display duly connected to the microcontroller, he must enter the password by the keypad. If it is matched with the stored password in the EEPROM retrieved by the microcontroller it delivers logic high at pin38 and 37 to either to open or close the door. For the purpose of the output verification we can use two lamps to indicate door opening and closing.
For IP configuration:

venkata@venkata:/etc/network$ ls
if-down.d if-post-down.d if-pre-up.d if-up.d interfaces interfaces.d run
venkata@venkata:/etc/network$ cd interfaces.d/
venkata@venkata:/etc/network/interfaces.d$ cd ..
venkata@venkata:/etc/network$ vim interfaces

[1]+ Stopped vim interfaces
venkata@venkata:/etc/network$
venkata@venkata:/etc/network$
venkata@venkata:/etc/network$ ll
total 40
drwxr-xr-x 7 root root 4096 Apr 17 2014 ./
drwxr-xr-x 151 root root 12288 Mar 8 16:54 ../
drwxr-xr-x 2 root root 4096 Apr 11 2016 if-down.d/
drwxr-xr-x 2 root root 4096 May 6 2016 if-post-down.d/
drwxr-xr-x 2 root root 4096 May 6 2016 if-pre-up.d/
drwxr-xr-x 2 root root 4096 Feb 19 17:46 if-up.d/
-rw-r--r-- 1 root root 82 Aug 20 2015 interfaces
drwxr-xr-x 2 root root 4096 Apr 4 2014 interfaces.d/
lrwxrwxrwx 1 root root 12 Aug 20 2015 run -> /run/network/
venkata@venkata:/etc/network$
venkata@venkata:/etc/network$ sudo su
[sudo] password for venkata:
root@venkata:/etc/network# vim interfaces
root@venkata:/etc/network#
root@venkata:/etc/network#
root@venkata:/etc/network#
root@venkata:/etc/network#
root@venkata:/etc/network#
root@venkata:/etc/network#
root@venkata:/etc/network#
root@venkata:/etc/network# sync

### Principle of operation of EEPROM
The EEPROM uses the principle same as that of the UV-EPROM. The electrons which are trapped in a floating gate will modify the characteristics of the cell, so instead of that logic “0” or logic “1” will be stored.
EEPROM is the memory device which implements the fewest standards in cell design. Most of the common cells are composed of two transistors. In this the storage transistor has the floating gate that will trap the electrons. Apart from that there is an access transistor which is used in the operation. In EPROM , cell is erased when electrons are removed from the floating gate, whereas in EEPROM , cell is erased when electrons are trapped in the floating cell.
There are two distinct EEPROM families: serial and parallel access. The serial access represents 90 percent of the overall EEPROM in market, where as the parallel access EEPROMs is about 10 percent.
The Linux I2C subsystem
The Linux I2C subsystem is the interface through which the system running Linux can interact with devices connected on the system’s I2C bus. It is designed in such a manner that the system running Linux is always the I2C master. It consists of the following subsections.
I2C adapter: There can be multiple I2C buses on the board, so each bus on the system is represented in Linux using the struct i2c_adapter (defined in include/linux/i2c.h). The following are the important fields present in this structure.
bus number: Each bus in the system is assigned a number that is present in the I2C adapter structure which represents it.
I2C algorithm: Each I2C bus operates with a certain protocol for communicating between devices. The algorithm that the bus uses is defined by this field. There are currently three algorithms for the I2C bus, which are pca, pcf and bitbanging. These algorithms are used to communicate with devices when the driver requests to write or read data from the device.
http://opensourceforu.com/2015/01/writing-i2c-clients-in-linux/

# 6 Stages of Linux Boot Process (Startup Sequence)
by Ramesh Natarajan on February 7, 2011
Tweet

Press the power button on your system, and after few moments you see the Linux login prompt.
Have you ever wondered what happens behind the scenes from the time you press the power button until the Linux login prompt appears?
The following are the 6 high level stages of a typical Linux boot process.
### 1. BIOS
- BIOS stands for Basic Input/Output System
- Performs some system integrity checks
- Searches, loads, and executes the boot loader program.
- It looks for boot loader in floppy, cd-rom, or hard drive. You can press a key (typically F12 of F2, but it depends on your system) during the BIOS startup to change the boot sequence.
- Once the boot loader program is detected and loaded into the memory, BIOS gives the control to it.
- So, in simple terms BIOS loads and executes the MBR boot loader.
### 2. MBR
- MBR stands for Master Boot Record.
- It is located in the 1st sector of the bootable disk. Typically /dev/hda, or /dev/sda
- MBR is less than 512 bytes in size. This has three components 1) primary boot loader info in 1st 446 bytes 2) partition table info in next 64 bytes 3) mbr validation check in last 2 bytes.
- It contains information about GRUB (or LILO in old systems).
- So, in simple terms MBR loads and executes the GRUB boot loader.
### 3. GRUB
- GRUB stands for Grand Unified Bootloader.
- If you have multiple kernel images installed on your system, you can choose which one to be executed.
- GRUB displays a splash screen, waits for few seconds, if you don’t enter anything, it loads the default kernel image as specified in the grub configuration file.
- GRUB has the knowledge of the filesystem (the older Linux loader LILO didn’t understand filesystem).
- Grub configuration file is /boot/grub/grub.conf (/etc/grub.conf is a link to this). The following is sample grub.conf of CentOS.
  #boot=/dev/sda
  default=0
  timeout=5
  splashimage=(hd0,0)/boot/grub/splash.xpm.gz
  hiddenmenu
  title CentOS (2.6.18-194.el5PAE)
  root (hd0,0)
  kernel /boot/vmlinuz-2.6.18-194.el5PAE ro root=LABEL=/
  initrd /boot/initrd-2.6.18-194.el5PAE.img
- As you notice from the above info, it contains kernel and initrd image.
- So, in simple terms GRUB just loads and executes Kernel and initrd images.
### 4. Kernel
- Mounts the root file system as specified in the “root=” in grub.conf
- Kernel executes the /sbin/init program
- Since init was the 1st program to be executed by Linux Kernel, it has the process id (PID) of 1. Do a ‘ps -ef | grep init’ and check the pid.
- initrd stands for Initial RAM Disk.
- initrd is used by kernel as temporary root file system until kernel is booted and the real root file system is mounted. It also contains necessary drivers compiled inside, which helps it to access the hard drive partitions, and other hardware.
### 5. Init
- Looks at the /etc/inittab file to decide the Linux run level.
- Following are the available run levels
  - 0 – halt
  - 1 – Single user mode
  - 2 – Multiuser, without NFS
  - 3 – Full multiuser mode
  - 4 – unused
  - 5 – X11
  - 6 – reboot
- Init identifies the default initlevel from /etc/inittab and uses that to load all appropriate program.
- Execute ‘grep initdefault /etc/inittab’ on your system to identify the default run level
- If you want to get into trouble, you can set the default run level to 0 or 6. Since you know what 0 and 6 means, probably you might not do that.
- Typically you would set the default run level to either 3 or 5.
### 6. Runlevel programs
- When the Linux system is booting up, you might see various services getting started. For example, it might say “starting sendmail …. OK”. Those are the runlevel programs, executed from the run level directory as defined by your run level.
- Depending on your default init level setting, the system will execute the programs from one of the following directories.
  - Run level 0 – /etc/rc.d/rc0.d/
  - Run level 1 – /etc/rc.d/rc1.d/
  - Run level 2 – /etc/rc.d/rc2.d/
  - Run level 3 – /etc/rc.d/rc3.d/
  - Run level 4 – /etc/rc.d/rc4.d/
  - Run level 5 – /etc/rc.d/rc5.d/
  - Run level 6 – /etc/rc.d/rc6.d/
- Please note that there are also symbolic links available for these directory under /etc directly. So, /etc/rc0.d is linked to /etc/rc.d/rc0.d.
- Under the /etc/rc.d/rc*.d/ directories, you would see programs that start with S and K.
- Programs starts with S are used during startup. S for startup.
- Programs starts with K are used during shutdown. K for kill.
- There are numbers right next to S and K in the program names. Those are the sequence number in which the programs should be started or killed.
- For example, S12syslog is to start the syslog deamon, which has the sequence number of 12. S80sendmail is to start the sendmail daemon, which has the sequence number of 80. So, syslog program will be started before sendmail.
There you have it. That is what happens during the Linux boot process.
For IP configuration:
go to the bellow directory

root@venkata:/etc/network/interfaces.d# lsblk
NAME MAJ:MIN RM SIZE RO TYPE MOUNTPOINT
sda 8:0 0 465.8G 0 disk
├─sda1 8:1 0 47.7G 0 part /
├─sda2 8:2 0 1K 0 part
├─sda3 8:3 0 46.6G 0 part
├─sda5 8:5 0 3.8G 0 part [SWAP]
└─sda6 8:6 0 142.1G 0 part /home
sdb 8:16 1 7.4G 0 disk
├─sdb1 8:17 1 41.8M 0 part /media/venkata/boot
└─sdb2 8:18 1 7.4G 0 part /media/venkata/b4ea8e46-fe87-4ddd-9e94-506c37005ac5
root@venkata:/etc/network/interfaces.d# cd /media/venkata/b4ea8e46-fe87-4ddd-9e94-506c37005ac5
root@venkata:/media/venkata/b4ea8e46-fe87-4ddd-9e94-506c37005ac5# cd etc/n
nanorc netconfig network/ networks newt/ nsswitch.conf
root@venkata:/media/venkata/b4ea8e46-fe87-4ddd-9e94-506c37005ac5# cd etc/net
netconfig network/ networks
root@venkata:/media/venkata/b4ea8e46-fe87-4ddd-9e94-506c37005ac5# cd etc/net
netconfig network/ networks
root@venkata:/media/venkata/b4ea8e46-fe87-4ddd-9e94-506c37005ac5# cd etc/network/interfaces
bash: cd: etc/network/interfaces: Not a directory
root@venkata:/media/venkata/b4ea8e46-fe87-4ddd-9e94-506c37005ac5# vi etc/network/interfaces
modify interfaces like bellow
 auto eth0
 iface eth0 inet static
 address 172.16.9.93
iface eth0 inet manual

 allow-hotplug wlan0
 iface wlan0 inet manual
 wpa-conf /etc/wpa_supplicant/wpa_supplicant.conf

 allow-hotplug wlan1
 16 iface wlan0 inet manual
 wpa-conf /etc/wpa_supplicant/wpa_supplicant.conf

wpa-conf /etc/wpa_supplicant/wpa_supplicant.conf
root@venkata:/etc/network# sync

Raspberry Pi 3 credentials:
user name : pi
password: pi
usb to serieal cable information :
 red power, black ground, white RX into USB port, and green TX out of the USB port

Issues:
1. i2c_eeprom2: loading out-of-tree module taints kernel.
2.rmmod: ERROR: Module i2c_eeprom is not currently loaded.
3. rmmod: ERROR: Module i2c_eeprom is in use
4.Failed to open /dev/eeprom24c02b
5.-bash: ./eeprom11: No such file or directory
Link for proc fs:
http://www.embetronicx.com/tutorials/linux/device-drivers/procfs-in-linux/
Link for sysfs:
http://opensourceforu.com/2015/05/talking-to-the-kernel-through-sysfs/
Link for mmap:
http://www.tutorialsdaddy.com/linux-device-drivers/mmap/
https://coherentmusings.wordpress.com/2014/06/10/implementing-mmap-for-transferring-data-from-user-space-to-kernel-space/
Link for sysfs:
https://github.com/blue119/kernel_user_space_interfaces_example/blob/master/mmap_kernel.c

link for linux drivers:
https://labs.mwrinfosecurity.com/assets/BlogFiles/mwri-mmap-exploitation-whitepaper-2017-09-18.pdf
MMAP:
Thinking that may be the ioctl() call and the context switch is the reason i have to use delays and this is going slow, i decided to look into ways of transferring data faster between the user and kernel space, instead of using an ioctl() call. An mmap() implementation in a driver or a memory mapping between user and kernel space is the fastest way to transfer data. This approach doesn’t incur a context switch nor a memory buffer copying. Below is a sample code showing how a mmap() implementation for a driver is done.
Pfn:
The page frame number corresponding to the physical address to which the virtual address should be mapped
# Clang - Features and Goals
This page describes the features and goals of Clang in more detail and gives a more broad explanation about what we mean. These features are:
End-User Features:
- Fast compiles and low memory use
- Expressive diagnostics
- GCC compatibility
Utility and Applications:
- Library based architecture
- Support diverse clients
- Integration with IDEs
- Use the LLVM 'BSD' License
Internal Design and Implementation:
- A real-world, production quality compiler
- A simple and hackable code base
- A single unified parser for C, Objective C, C++, and Objective C++
- Conformance with C/C++/ObjC and their variants
## End-User Features
### Fast compiles and Low Memory Use
A major focus of our work on clang is to make it fast, light and scalable. The library-based architecture of clang makes it straight-forward to time and profile the cost of each layer of the stack, and the driver has a number of options for performance analysis. Many detailed benchmarks can be found online.
Compile time performance is important, but when using clang as an API, often memory use is even moreso: the less memory the code takes the more code you can fit into memory at a time (useful for whole program analysis tools, for example).
In addition to being efficient when pitted head-to-head against GCC in batch mode, clang is built with a library based architecture that makes it relatively easy to adapt it and build new tools with it. This means that it is often possible to apply out-of-the-box thinking and novel techniques to improve compilation in various ways.
### Expressive Diagnostics
In addition to being fast and functional, we aim to make Clang extremely user friendly. As far as a command-line compiler goes, this basically boils down to making the diagnostics (error and warning messages) generated by the compiler be as useful as possible. There are several ways that we do this, but the most important are pinpointing exactly what is wrong in the program, highlighting related information so that it is easy to understand at a glance, and making the wording as clear as possible.
Here is one simple example that illustrates the difference between a typical GCC and Clang diagnostic:
  $ gcc-4.2 -fsyntax-only t.c
  t.c:7: error: invalid operands to binary + (have 'int' and 'struct A')
  $ clang -fsyntax-only t.c
  t.c:7:39: error: invalid operands to binary expression ('int' and 'struct A')
    return y + func(y ? ((SomeA.X + 40) + SomeA) / 42 + SomeA.X : SomeA.X);
        ~~~~~~~~~~~~~~ ^ ~~~~~
Here you can see that you don't even need to see the original source code to understand what is wrong based on the Clang error: Because Clang prints a caret, you know exactly which plus it is complaining about. The range information highlights the left and right side of the plus which makes it immediately obvious what the compiler is talking about, which is very useful for cases involving precedence issues and many other situations.
Clang diagnostics are very polished and have many features. For more information and examples, please see the Expressive Diagnostics page.
### GCC Compatibility
GCC is currently the defacto-standard open source compiler today, and it routinely compiles a huge volume of code. GCC supports a huge number of extensions and features (many of which are undocumented) and a lot of code and header files depend on these features in order to build.
While it would be nice to be able to ignore these extensions and focus on implementing the language standards to the letter, pragmatics force us to support the GCC extensions that see the most use. Many users just want their code to compile, they don't care to argue about whether it is pedantically C99 or not.
As mentioned above, all extensions are explicitly recognized as such and marked with extension diagnostics, which can be mapped to warnings, errors, or just ignored.
## Utility and Applications
### Library Based Architecture
A major design concept for clang is its use of a library-based architecture. In this design, various parts of the front-end can be cleanly divided into separate libraries which can then be mixed up for different needs and uses. In addition, the library-based approach encourages good interfaces and makes it easier for new developers to get involved (because they only need to understand small pieces of the big picture).
"The world needs better compiler tools, tools which are built as libraries. This design point allows reuse of the tools in new and novel ways. However, building the tools as libraries isn't enough: they must have clean APIs, be as decoupled from each other as possible, and be easy to modify/extend. This requires clean layering, decent design, and keeping the libraries independent of any specific client."
Currently, clang is divided into the following libraries and tool:
- libsupport - Basic support library, from LLVM.
- libsystem - System abstraction library, from LLVM.
- libbasic - Diagnostics, SourceLocations, SourceBuffer abstraction, file system caching for input source files.
- libast - Provides classes to represent the C AST, the C type system, builtin functions, and various helpers for analyzing and manipulating the AST (visitors, pretty printers, etc).
- liblex - Lexing and preprocessing, identifier hash table, pragma handling, tokens, and macro expansion.
- libparse - Parsing. This library invokes coarse-grained 'Actions' provided by the client (e.g. libsema builds ASTs) but knows nothing about ASTs or other client-specific data structures.
- libsema - Semantic Analysis. This provides a set of parser actions to build a standardized AST for programs.
- libcodegen - Lower the AST to LLVM IR for optimization & code generation.
- librewrite - Editing of text buffers (important for code rewriting transformation, like refactoring).
- libanalysis - Static analysis support.
- clang - A driver program, client of the libraries at various levels.
As an example of the power of this library based design.... If you wanted to build a preprocessor, you would take the Basic and Lexer libraries. If you want an indexer, you would take the previous two and add the Parser library and some actions for indexing. If you want a refactoring, static analysis, or source-to-source compiler tool, you would then add the AST building and semantic analyzer libraries.
For more information about the low-level implementation details of the various clang libraries, please see the clang Internals Manual.
### Support Diverse Clients
Clang is designed and built with many grand plans for how we can use it. The driving force is the fact that we use C and C++ daily, and have to suffer due to a lack of good tools available for it. We believe that the C and C++ tools ecosystem has been significantly limited by how difficult it is to parse and represent the source code for these languages, and we aim to rectify this problem in clang.
The problem with this goal is that different clients have very different requirements. Consider code generation, for example: a simple front-end that parses for code generation must analyze the code for validity and emit code in some intermediate form to pass off to a optimizer or backend. Because validity analysis and code generation can largely be done on the fly, there is not hard requirement that the front-end actually build up a full AST for all the expressions and statements in the code. TCC and GCC are examples of compilers that either build no real AST (in the former case) or build a stripped down and simplified AST (in the later case) because they focus primarily on codegen.
On the opposite side of the spectrum, some clients (like refactoring) want highly detailed information about the original source code and want a complete AST to describe it with. Refactoring wants to have information about macro expansions, the location of every paren expression '(((x)))' vs 'x', full position information, and much more. Further, refactoring wants to look across the whole program to ensure that it is making transformations that are safe. Making this efficient and getting this right requires a significant amount of engineering and algorithmic work that simply are unnecessary for a simple static compiler.
The beauty of the clang approach is that it does not restrict how you use it. In particular, it is possible to use the clang preprocessor and parser to build an extremely quick and light-weight on-the-fly code generator (similar to TCC) that does not build an AST at all. As an intermediate step, clang supports using the current AST generation and semantic analysis code and having a code generation client free the AST for each function after code generation. Finally, clang provides support for building and retaining fully-fledged ASTs, and even supports writing them out to disk.
Designing the libraries with clean and simple APIs allows these high-level policy decisions to be determined in the client, instead of forcing "one true way" in the implementation of any of these libraries. Getting this right is hard, and we don't always get it right the first time, but we fix any problems when we realize we made a mistake.
### Integration with IDEs
We believe that Integrated Development Environments (IDE's) are a great way to pull together various pieces of the development puzzle, and aim to make clang work well in such an environment. The chief advantage of an IDE is that they typically have visibility across your entire project and are long-lived processes, whereas stand-alone compiler tools are typically invoked on each individual file in the project, and thus have limited scope.
There are many implications of this difference, but a significant one has to do with efficiency and caching: sharing an address space across different files in a project, means that you can use intelligent caching and other techniques to dramatically reduce analysis/compilation time.
A further difference between IDEs and batch compiler is that they often impose very different requirements on the front-end: they depend on high performance in order to provide a "snappy" experience, and thus really want techniques like "incremental compilation", "fuzzy parsing", etc. Finally, IDEs often have very different requirements than code generation, often requiring information that a codegen-only frontend can throw away. Clang is specifically designed and built to capture this information.
### Use the LLVM 'BSD' License
We actively intend for clang (and LLVM as a whole) to be used for commercial projects, not only as a stand-alone compiler but also as a library embedded inside a proprietary application. The BSD license is the simplest way to allow this. We feel that the license encourages contributors to pick up the source and work with it, and believe that those individuals and organizations will contribute back their work if they do not want to have to maintain a fork forever (which is time consuming and expensive when merges are involved). Further, nobody makes money on compilers these days, but many people need them to get bigger goals accomplished: it makes sense for everyone to work together.
For more information about the LLVM/clang license, please see the LLVM License Description for more information.
## Internal Design and Implementation
### A real-world, production quality compiler
Clang is designed and built by experienced compiler developers who are increasingly frustrated with the problems that existing open source compilers have. Clang is carefully and thoughtfully designed and built to provide the foundation of a whole new generation of C/C++/Objective C development tools, and we intend for it to be production quality.
Being a production quality compiler means many things: it means being high performance, being solid and (relatively) bug free, and it means eventually being used and depended on by a broad range of people. While we are still in the early development stages, we strongly believe that this will become a reality.
### A simple and hackable code base
Our goal is to make it possible for anyone with a basic understanding of compilers and working knowledge of the C/C++/ObjC languages to understand and extend the clang source base. A large part of this falls out of our decision to make the AST mirror the languages as closely as possible: you have your friendly if statement, for statement, parenthesis expression, structs, unions, etc, all represented in a simple and explicit way.
In addition to a simple design, we work to make the source base approachable by commenting it well, including citations of the language standards where appropriate, and designing the code for simplicity. Beyond that, clang offers a set of AST dumpers, printers, and visualizers that make it easy to put code in and see how it is represented.
### A single unified parser for C, Objective C, C++, and Objective C++
Clang is the "C Language Family Front-end", which means we intend to support the most popular members of the C family. We are convinced that the right parsing technology for this class of languages is a hand-built recursive-descent parser. Because it is plain C++ code, recursive descent makes it very easy for new developers to understand the code, it easily supports ad-hoc rules and other strange hacks required by C/C++, and makes it straight-forward to implement excellent diagnostics and error recovery.
We believe that implementing C/C++/ObjC in a single unified parser makes the end result easier to maintain and evolve than maintaining a separate C and C++ parser which must be bugfixed and maintained independently of each other.
### Conformance with C/C++/ObjC and their variants
When you start work on implementing a language, you find out that there is a huge gap between how the language works and how most people understand it to work. This gap is the difference between a normal programmer and a (scary? super-natural?) "language lawyer", who knows the ins and outs of the language and can grok standardese with ease.
In practice, being conformant with the languages means that we aim to support the full language, including the dark and dusty corners (like trigraphs, preprocessor arcana, C99 VLAs, etc). Where we support extensions above and beyond what the standard officially allows, we make an effort to explicitly call this out in the code and emit warnings about it (which are disabled by default, but can optionally be mapped to either warnings or errors), allowing you to use clang in "strict" mode if you desire.
We also intend to support "dialects" of these languages, such as C89, K&R C, C++'03, Objective-C 2, etc.
Reply - Reply to All - Forward - More Actions

TRACE 32
## Introduction
Trace32 is in-circuit emulator and logic analyzer used for debugging embedded systems. Many embedded developers would like to see a higher level of standardization of the on-chip debug and trace logic as well as a reduction in pin count without any performance loss.
In this page, you can find a list of the most commonly used commands on Trace32:
## Function and variables:
Command	Description
d.l	Shows where the PC is.
d.l <Function Name>	Shows the given function. This is window will not update when PC changes.
var.local	List of all local variables
var.frame	List of all local variables and call stack
var.view	Opens a watch window to check the value of variable
v.v %e	Opens a watch window to check the value of variables. The values are updated while the processor is running.
v.f	View the current stack frame
v <Variable> = x	Assigns the value x to the variable. It can be done also with a double click on the variable

## Breakpoints
Command	Description
b.l	Shows the list of breakpoints
b.s func_name	Add breakpoint at func_name
b.set e:<Function Name>	Insert a breakpoint during the Execution(CPU Access Enabled)

## Symbols
Command	Description
y.b	List of all symbols
y.list.source	List of source files
y.spath.list	List of direction of source. More directories can be added from here.
y.load.source	Loads the single source file
y.b.f	Browse all function symbols
y.b.f shim*	Browse all function starting with shim (e.g. shim_init)

## Debugging the Debugger
Command	Description
Data.log	Opens a window and shows some of the activity the debugger performs
Log.open file_id	This starts a log file and logs all the hardware commands being issued from the command line, within command files etc..,
Log.close	This will close the log file you opened above

## Common Trace32 Commands
Other basic commands are as follows:
Command	Description
run mjnload	Loads a build onto the target
run jload	Loads the symbols
go	Starts the target
sys.d	System down
sys.u	System up
run jnreset	Resets the target
go initial_task	Display the CPU Registers
t.l tcb_ptr	View SW task information. E.g. Registers, stack. tcb_ptr is the first column of task window in hex format

Dumping Memory Regions Dumping into window
        Data.dump 0x84002310 – 0x85430234
Dumping into text file
        d.save.binary C:\Dump.bin 0x84002310 – 0x85430234
View Image
        d.image
Viewing Registers
        Register /spotlight - Register window will open with colorized changes
Qualcomm specific debugging:

Once a crashdump is loaded run this command will show registers value at moment of crash
        v.v QURT_error_info
By setting register values from Qurt_error_info to current registers
        r.s $registername value
        Ex: r.s R0 0x80
Once all registers set, click Stack frame with locals to see stack trace leading to crash.
For More Commands: