  ARM Instruction Set
        By,
        T.Venkata Rao.

---
Agenda
- The ARM Instruction Set.
- The Thumb Instruction Set.

---
  Instructions
- Instructions process data held in registers and access memory with load and store instructions
- Classes of instructions:
  - Data processing
  - Branch instructions
  - Load-store instructions
  - Software interrupt instruction
  - Program status register instructions

---
  ARM data types
- Word is 32 bits long.
- Word can be divided into four 8-bit bytes.
- ARM addresses can be 32 bits long.
- Address refers to byte.
- Address 4 starts at byte 4.
- Can be configured at power-up as either little- or big-endian mode

---
 Data Processing Instructions.
Manipulate data within registers
  - MOVE instructions
  - Arithmetic instructions
  - Multiply instructions
  - Logical instructions
  - Comparison instructions
Suffix S on data processing instructions updates flags in CPSR

---
 Move instruction
MOV Rd, N
  - Rd : destination register
  - N : can be an immediate value or source register
  - Example: mov r7, r5
- MVN Rd, N
  - Move into Rd not of the 32-bit value from source

---
 Using Barrel Shifter
- Enables shifting 32-bit operand in one of the source registers left or right by a specific number of positions within the cycle time of instruction
- Basic Barrel shifter operations
  - Shift left, shift right, rotate right
- Facilitates fast multiply, division and increases code density
- Example: mov r7, r5, LSL #2
  - Multiplies content of r5 by 4 and puts result in r7

---
 Arithmetic Instructions
- Implements 32 bit addition and subtraction
  - 3-operand form
  - Examples:
    - SUB r0, r1, r2
      - Subtract value stored in r2 from that of r1 and store in r0
    - SUBS r1, r1, #1
      - Subtract 1 from r1 and store result in r1 and update Z and C flags

---
 Arithmetic Instructions With Barrel Shifter
- Use of barrel shifter with arithmetic and logical instructions increases the set of possible available operations
- Example
  - ADD r0,r1,r1 LSL#1
  - Register r1 is shifted to the left by 1, then it is added with r1 and the result ( 3 times r1) is stored in r0.

---
Multiply Instructions
- Multiply contents of a pair of registers
  - Long multiply generates 64 bit result
- Examples:
  - MUL r0, r1,r2
    - Contents of r1 and r2 multiplied and put in r0
  - UMULL r0,r1,r2,r3
    - Unsigned multiply with result stored in r0 and r1
- Number of cycles taken for execution of multiply instruction depends upon processor implementation

---
Multiply and Accumulate
- Result of multiplication can be accumulated with content of another register
  - MLA Rd, Rm, Rs, Rn
    - Rd =(Rm*Rs) + Rn
  - UMLAL Rdlo, Rdhi, Rm, Rs
    - [Rdhi,Rdlo] = [Rdhi,Rdlo] + (Rm*Rs)

---
Compare Instructions
- Enables comparison of 32 bit values
  - Updates CPSR flags but do not affect other registers
  - Examples
    - CMP r0,r9
      - Flags set as a result of r0 - r9
    - TEQ r0,r9
      - Flags set as a result r0 ex-or r9
    - TST r0,r9
      - Flags set as a result of r0 & r9

---
Load-Store Instructions
- Transfers data between memory and processor registers
  - Single register transfer
    - Data types supported are signed and unsigned words (32 bits), half-words, bytes
  - Multiple-register transfer
    - Transfer multiple registers between memory and the processor in a single instruction
  - Swap
    - Swaps content of a memory location with the contents of a register

---
Single Transfer Instructions
- Load & Store data on a boundary alignment
  - LDR, LDRH, LDRB :
    - load (word, half-word, byte)
  - STR, STRH, STRB :
    - store (word, half-word, byte)
- Supports different addressing modes:
  - Register indirect : LDR r0,[r1]
  - Immediate: LDR r0,[r1,#4]
    - 12-bit offset added to the base register
  - Register operation: LDR r0,[r1,-r2]
    - Address calculated using base register and another register

---
More Addressing Modes
- Scaled
  - Address is calculated using the base address register and a barrel shift operation
- Pre & Post Indexing
  - Pre-index with write back: LDR r0,[r1,#4]!
    - Updates the address base register with new address
  - Post index: LDR r0,[r1],#4
    - Updates the address register after address is used

---
Multiple Register Transfer
- Load-store multiple instructions transfer multiple register contents between memory and the processor in a single instruction
- More efficient – for moving blocks of memory and saving and restoring context and stack
- These instructions can increase interrupt latency
  - Usually instruction executions are not interrupted by ARM
Multiple Byte Load-Store :
- Any subset of current bank of registers can be transferred to memory or fetched from memory
  - LDM
  - SDM
  - The base register Rn determines source or destination address

---
Some Stack Instructions
- Full Ascending
  - LDMFA : translates to LDMDA (POP)
  - STMFA : translates to STMIB (PUSH)
  - SP points to last item in stack
- Empty Descending
  - LDMED : translates to LDMIB (POP)
  - STMED : translates to STMIA (PUSH)
  - SP points to first unused location

---
SWAP Instruction
- Special case of load store instruction
- Swap instructions:
  - SWP : swap a word between memory and register
  - SWPB : swap a byte between memory and register
- Useful for implementing synchronization primitives like semaphore

---
Control Flow Instructions
- Branch Instructions
- Conditional Branches
- Conditional Execution
- Branch and Link instructions
- Subroutine Return Instructions

---
Branch Instruction
- Branch instruction : B label
  - Example: B forward
  - Address label is stored in the instruction as a signed pc-relative offset
- Conditional Branch: B<cond> label
  - Example: BNE loop
  - Branch has a condition associated with it and executed if condition codes have the correct value

---
Conditional Execution
- An unusual feature of ARM instruction set is that conditional execution applies not only to branches but to all ARM instructions
- Example: ADDEQ r0,r1,r2
  - Instruction will only be executed when the zero flag is set to 1

---
Branch & Link Instruction
- Perform a branch, save the address following the branch in the link register, r14
- Example: BL subroutine
- For nested subroutine, push r14 and some work registers required to be saved onto a stack in memory
  - Example
    BL sub1
    …
    STMFD r13!,{r0-r2,r14}
    BL sub2
    …..

---
Software Interrupt Instruction (SWI)
- A software Interrupt instruction causes a software interrupt exception, which provides a mechanism for applications to OS routines
- Instruction: SWI {<cond>} SWI_number
- When the processor executes an SWI instruction, it sets the program counter pc to the offset 0x8 in the vector table
- Instruction also forces the processor mode to SVC, which allows an operating system routine to execute
- SWI is typically executed in user mode
- Instruction forces processor mode to supervisor (SVC) – this allows an OS routine to be executed in privileged mode
- Each SWI has an associated SWI number which is used to represent a particular function call or feature
- Parameter passing – through registers; Return value is also passed using registers

---
Program Status Register Instructions
- Two instructions to control PSR directly
- MRS – transfers contents of either cpsr or spsr into a register
- MSR – transfers contents of register to cpsr or spsr
Example:
    - Enabling IRQ interupt
      - PRE cpsr = nzcvqIFt_SVC
        MRS r1,CPSR
        BIC r1,r1,#0x80
        MSR cpsr, r1
      - POST cpsr =nzcvqiFt_SVC
      - Instructions in SVC mode

---
Co-processor Instructions
- Used to extend the instruction set
  - Used by cores with a co-processor
  - Co-processor specific operations
- Syntax: co-processor data processing
  - CDP{<cond>} cp,opcode1, Cd, Cn, Cm, {,opcode2}
    - Cp represents co-processor number between p0 to p15
    - opcode field describes co-processor operation
    - Cd, Cn, Cm co-processor registers
- Also co-processor register transfer and memory transfer instructions

---
Thumb instructions
Thumb:
- Thumb encodes a subset of the 32 bit instruction set into a 16-bit subspace
- Thumb has higher performance than ARM on a processor with a 16-bit data bus
- Thumb has higher code density
  - For memory constrained embedded system
  Thumb instructions:
- Only low registers r0 to r7 fully accessible
  - Higher registers accessible with MOV, ADD, CMP instructions
- Only branch instruction can be conditionally executed
- Barrel shift operations are separate instructions

---
ARM-Thumb Inter-working
- To call a thumb routine from an ARM routine the core has to change state
  - Changing T bit in CPSR
- BX and BLX instruction can be used for the switch
  - Example : BX r0 ; BLX r0
  - Enters Thumb state if bit 0 of the address in Rn is set to binary 1; otherwise it enters ARM state
  - Thumb

---
ARMv5E Extensions
- Extensions to facilitate signal processing operations
- Supports
  - Signed multiply accumulate instruction
  - Saturation Arithmetic
  - Greater flexibility and efficiency when manipulating 16 bit values for applications such as 16-it digital audio processing
Saturation Arithmetic:
- Normal ARM arithmetic instructions wrap around when there is an overflow of an integer value
- Using ARMv5E instructions you can saturate the result
  - Once the highest number is exceeded the result remains at the maximum value
  - Minimum value does not change on underflow
- Example Instructions: QADD, QSUB