        Touch screen

For reference:

matthewhalpern.com/publications/mosaic-ispass-2015.pdf

https://books.google.co.in/books?id=JxyB_p1g6uMC&pg=PA195&lpg=PA195&dq=android+touch+driver+flow&source=bl&ots=CHaydDxSXQ&sig=HwplR3mfBGK9MYR8eorf3Td89yE&hl=en&sa=X&ved=0ahUKEwiI5t347JTWAhWKp48KHQVoCIUQ6AEIVTAH#v=onepage&q=android%20touch%20driver%20flow&f=false

http://processors.wiki.ti.com/index.php/TI-Android-GingerBread-2.3.4-DevKit-
2.1_PortingGuides#Touchscreen

http://ww1.microchip.com/downloads/en/DeviceDoc/AR1020-AR1021-LINUX-SPI-I2C-V102.pdf

https://android.googlesource.com/kernel/bcm/
+/23d376ef33aa4c500a5ea24a290f029d5f8e2de3/drivers/input/touchscreen/egalax_i2c_ts.c

https://linux.die.net/man/1/objdump

https://android.googlesource.com/kernel/bcm/
+/55040d0cfa091003fb7840fd057e109969ac2440/drivers/input/touchscreen/synaptics_i2c_rmi.c

link for touchscreen working:
https://www.digikey.in/en/articles/techzone/2012/sep/from-touch-to-call-tracing-the-path-of-a-touch-gesture

Multi-touch (MT) protocol : which allows kernel drivers to report details for an arbitrary number of contacts.

1.The protocol is divided into two types, depending on the capabilities of the
hardware.

Type A: For devices handling anonymous contacts (type A).
the protocol describes how to send the raw data for all contacts to the receiver.

Type B:

For ft5406 data sheet:
http://www.datasheetspdf.com/pdf/897575/FocalTechSystems/FT5406/3.

Linux Input Subsystem Introduction

The three major elements of the input subsystem are:
Input Core
Event Handlers
Input Device Drivers
This subsystem is part of the kernel because these devices usually are accessed through special hardware interfaces (such as serial ports, PS/2, SPI, I2C and USB), which are protected and managed by the kernel itself.

The kernel then exposes the user input in a consistent, device-independent way to user space through a range of defined APIs.
keybdev
mousedev
joydev
evdev

The evdev for example exposes the raw events with a timestamp to user space through a collection of character device nodes - one character device node per logical input device. (/dev/input/eventX)

EV_ABS / Serio / USB HID / Bluetooth / HID / I2C / SPI / GPIO / PS/2 / Mouse / Keyboard / Touch / Controller / Serio / Mouse / Keyboard / Bluetooth / Mouse / Keyboard / I2C Touch / Controller / SPI / Accelero / meter / Rotary / Input / Device Drivers / Input CORE / Input Event Handlers / mousedev, joydev, keyboard, / evdev / Virtual / Terminal / Console / X Windows / /dev/input/mice / /dev/input/eventX / /dev/input/js / Qt / Custom Application / User Space / Kernel Space / Kernel Space / Hardware / Keyboard / Input	Absolute Axis Events	Touch Screen, Joysticks

Each LCD features a full color 800 x 480 capacitive touch display that connects to the Pi via an included adapter board which handles all of your power and signal conversion needs.
Note that while the normal path is from low-level hardware to drivers, drivers to input core, input core to handler and handler to user space, there usually is a return path as well.

DSI interface driver path:
iinux/drivers/gpu/drm/panel/panelrpitouchscreen

Required API's:

* kzalloc() allocates kernel memory like kmalloc(), but it also zero-initializes the allocated memory. devm_kzalloc() is managed kzalloc(). The memory allocated with managed functions is associated with the device. When the device is detached from the system or the driver for the device is unloaded, that memory is freed automatically. If multiple managed resources (memory or some other resource) were allocated for the device, the resource allocated last is freed first.

NAME: devm_kzalloc - Resource-managed kzalloc / SYNOPSIS: void * devm_kzalloc(struct device * dev, size_t size, gfp_t gfp); / ARGUMENTS : / dev / Device to allocate memory for / size / Allocation size / gfp / Allocation gfp flags / DESCRIPTION / Managed kzalloc. Memory allocated with this function is automatically freed on driver / detach. Like all other devres resources, guaranteed alignment is unsigned long long. / RETURNS / Pointer to allocated memory on success, NULL on failure.

* Name
kthread_run — create and wake a thread.
Synopsis
kthread_run (threadfn, data, namefmt, ...);
Arguments
threadfn
the function to run until signal_pending(current).
data
data ptr for threadfn.
namefmt
printf-style name for the thread.
...
variable arguments
Description
Convenient wrapper for kthread_create followed by wake_up_process. Returns the kthread or ERR_PTR(-ENOMEM).
----------------------------------------------------------------------------
* Name
kthread_create — create a kthread.
Synopsis
struct task_struct * kthread_create (int (*threadfn(void *data),
void * data, const char namefmt[], ...);
Arguments
threadfn
the function to run until signal_pending(current).
data
data ptr for threadfn.
namefmt[]
printf-style name for the thread.
...
variable arguments
Description
This helper function creates and names a kernel thread. The thread will be stopped: use wake_up_process to start it. See also kthread_run, kthread_create_on_cpu.
When woken, the thread will run threadfn() with data as its argument. threadfn can either call do_exit directly if it is a standalone thread for which noone will call kthread_stop, or return when 'kthread_should_stop' is true (which means kthread_stop has been called). The return value should be zero or a negative error number; it will be passed to kthread_stop.
Returns a task_struct or ERR_PTR(-ENOMEM).

* NAME
kthread_should_stop − should this kthread return now?
SYNOPSIS
int kthread_should_stop(void);
ARGUMENTS
void
no arguments
DESCRIPTION
When someone calls kthread_stop on your kthread, it will be woken and this will return true. You should then return, and your return value will be passed through to kthread_stop.
-------------------------------------------------------------------------------------------
* NAME
kthread_stop − stop a thread created by kthread_create.
SYNOPSIS
int kthread_stop(struct task_struct * k);
ARGUMENTS
k
thread created by kthread_create.
DESCRIPTION
Sets kthread_should_stop for k to return true, wakes it, and waits for it to exit. Your threadfn must not call do_exit itself if you use this function! This can also be called after kthread_create instead of calling wake_up_process: the thread will exit without calling threadfn.
Returns the result of threadfn, or −EINTR if wake_up_process was never called.
---------------------------------------------------------------------------------------------
* Name
__set_bit — Set a bit in memory
Synopsis
void __set_bit (long nr, volatile unsigned long * addr);
Arguments
long nrack frame .

the bit to set
volatile unsigned long * addr
the address to start counting from
Description
Unlike set_bit, this function is non-atomic and may be reordered. If it's called on the same region of memory simultaneously, the effect may be that only one operation succeeds.
---------------------------------------------------------------------------------------
* Name
msleep_interruptible — sleep waiting for signals
Synopsis
unsigned long msleep_interruptible (unsigned int msecs);

Arguments
msecs
Time in milliseconds to sleep for
----------------------------------------------------------------------------------------
* Hi Linus. On x86 and ia64, memcpy_fromio is protoyped as:
static inline void memcpy_fromio(void *dst, volatile void __iomem *src, int count)
ALSA does this (except on x86 and sparc32, so you don't see it):
int copy_to_user_fromio(void __user *dst, const void __iomem *src, size_t count)
[...]
        memcpy_fromio(bdevice node:/dev/eventX
user space
Event
handle
Kernel
space
kernel files: evdev.c, tsdev.c, joydev.c
, mousedev.c, keyboard.c, etc
i nput
core
kernel file:
driver/input/input.c
Keywords-input subsystem, S3C6410, driver
I.
I NTRODUCTION
The process of developing an input device driver has its
traditional method, that method always contains the
definition and realization of the devices’ operational
function pointers in the structure of file_operations, such as
open, read, write, ioctl, llseek and etc [1]. However, the
realization of the file_operations often occupied a lot of
development time, and it’s also an error-prone area. In order
to avoid doing this work, this paper designed a touch screen
driver based on Linux input subsystem and the S3C6410
platform, and a detailed test process was given to verify its
function.
II.
A N ANALYSIS OF THE INPUT SUBSYSTEM IN L INUX 2.6
KERNEL
A. Input subsystem’s analysis
The 2.6 edition of the Linux kernel introduced an input
subsystem framework. It’s on the same level of other
subsystems like file system and network system. The
introduction of the input subsystem makes it more efficient
to develop drive software of mouse, keyboard or touching
screen in Linux. Further study of the subsystems in the
Linux kernel shows that the system packed frequently used
function sets for specific hardware devices. Linux input
subsystem is constructed by input driver layer, input core
layer and input event handle layer [2]. And the structure
within the Linux system is illustrated in Fig.1.
The input driver layer control the specific hardware by
configuration of registers and interrupt process. The input
motion of input devices, such as click, press and touch, is
abstracted into an event, which will be reported to the input
core layer. And this part shall be developers’ work.
Input core layer connect two layers of input driver and
input
driver
hardware space
Figure.1.
input device drivers such as
touch screen, mouse, keyboard
Input devices
Structure of Linux input subsystemsuf, src, c);
--------------------------------------------------------------------------------------------
NAME	top
       offsetof - offset of a structure member
SYNOPSIS	top
       #include <stddef.h>

       size_t offsetof(type, member);ack frame .

DESCRIPTION	top
       The macro offsetof() returns the offset of the field member from the
       start of the structure type.

       This macro is useful because the sizes of the fields that compose a
       structure can vary across implementations, and compilers may insert
       different numbers of padding bytes between fields. Consequently, an
       element's offset is not necessarily given by the sum of the sizes of
       the previous elements.

       A compiler error will result if member is not aligned to a byte
       boundary (i.e., it is a bit field).
RETURN VALUE         top
       offsetof() returns the offset of the given member within the given
       type, in units of bytes.
CONFORMING TO         top
       POSIX.1-2001, POSIX.1-2008, C89, C99.
EXAMPLE         top
       On a Linux/i386 system, when compiled using the default gcc(1)
       options, the program below produces the following output:

        $ ./a.out
        offsets: i=0; c=4; d=8 a=16
        sizeof(struct s)=16

   Program source

       #include <stddef.h>
       #include <stdio.h>
       #include <stdlib.h>

       int
       main(void)
       {
        struct s {
        int i;
        char c;
        double d;
        char a[];
        };

        /* Output is compiler dependent */

        printf("offsets: i=%zd; c=%zd; d=%zd a=%zd\n",
        offsetof(struct s, i), offsetof(struct s, c),
        offsetof(struct s, d), offsetof(struct s, a));
        printf("sizeof(struct s)=%zd\n", sizeof(struct s));

        exit(EXIT_SUCCESS);
       }
COLOPHON         top
       This page is part of release 4.15 of the Linux man-pages project. A
       description of the project, information about reporting bugs, and the
       latest version of this page, can be found at
       https://www.kernel.org/doc/man-pages/.
----------------------------------------------------------------------------
NAME
input_mt_report_pointer_emulation - common pointer emulation
SYNOPSIS
void input_mt_report_pointer_emulation(struct input_dev * dev, bool use_count);
ARGUMENTS
dev
input device with allocated MT slots
use_count
report number of active contacts as finger count
DESCRIPTION
Performs legacy pointer emulation via BTN_TOUCH, ABS_X, ABS_Y and ABS_PRESSURE. Touchpad finger count is emulated if use_count is true.
The input core ensures only the KEY and ABS axes already setup for this device will produce output.

1.I2C Interface
1.1 CTPM interface to Host
Figure 1-1 shows how CTPM communicates with the Host, there are three kind of communication between CTPM and Host，we will introduce each communication in this section.

Transfer the data via I2C
Send interrupt when there is a valid touch
Host send Wakeup signal to CTPM

 Starting driver code
Have modified my dts as :

&i2c0 {
    pinctrl-names = "default";
    pinctrl-0 = <&i2c0_pins>;
    status = "okay";
    clock-frequency = <400000>;
    tps: tps@2d {
        reg = <0x2d>;
    };
        i2cdev0: ft5406@38 {
status = "okay"; compatible = "my_touch"; pinctrl-names = "default"; pinctrl-0 = <&edt_ft5406_ts_pins>; reg = <0x38>; interrupt-parent = <&gpio1>; interrupts = <21 1>; reset-gpios = <&gpio1 22 GPIO_ACTIVE_HIGH>; touchscreen-size-x = <800>; touchscreen-size-y = <480>; };

};

IRQ Numbers:

        Pin No.
        VSSA 40
NC 1
NC

1 1
Type
PWR

Name FT5206GE1	FT5306DE4 FT5406EE8 Type	Description

WAKE	27	33	46	I	External interrupt from the host
INT	28	34	47	O External interrupt to the host

For FT5406DQ9:

WAKE = 37
INT = 38

kernel build for rRNEL BUILDING

kernel build for raspberry pi 3 :
https://www.raspberrypi.org/documentation/linux/kernel/building.md

cd linux
KERNEL=kernel7
sudo make ARCH=arm CROSS_COMPILE=arm-linux-gnueabihf- menuconfig
sudo make ARCH=arm CROSS_COMPILE=arm-linux-gnueabihf- zImage modules dtbs

sudo cp mnt/fat32/$KERNEL.img mnt/fat32/$KERNEL-backup.img
sudo cp arch/arm/boot/zImage mnt/fat32/$KERNEL.img
sudo cp arch/arm/boot/dts/*.dtb mnt/fat32/
sudo cp arch/arm/boot/dts/overlays/*.dtb* mnt/fat32/overlays/
sudo cp arch/arm/boot/dts/overlays/README mnt/fat32/overlays/
sudo umount mnt/fat32
sudo umount mnt/ext4
sync